## Slide 1: Basic electronic component tester
Lukács Botond

## Slide 2: Goals
Finding resistors, capacitors, diodes and transistors pinout and approximate values in an automated way with a help of a microcontroller.
Plotting the transistors characteristic diagramm.
Automated testing.
Ease of use.

## Slide 3: Component identification steps

## Slide 4
Microcontroller
USB
Serial communication and power
Tester socket
ADC signals
Display
SPI
Start Switch
Status LED
DAC
SPI
Analog switch
Digital control signals
3 analog voltage signal
Selected signal
System block diagram

## Slide 5
The measuring circuit

## Slide 6: Circuit diagram

## Slide 7: Current control
The DAC only controls the voltage, so software based control is required
A P controller is used for this
This is required for the transistors characteristic diagram

## Slide 8: Displaying results

## Slide 9
Resistor testing
Chart: Resistor measurement error
| 47 | 56 | 100 | 220 | 360 | 540 | 1000 | 2200 | 4700 | 10000 | 33000 | 62000
Relative error compared to multimeter (%) | 11.7021 | 5.9246 | 7.2927 | 11.0092 | 11.7978 | 11.3971 | -9.1837 | 4.7179 | -7.5011 | -4.5764 | -13.3322 | -20.0161
Relative error compared to printed value (%) | 11.7021 | 5.3571 | 7.4 | 10 | 10.5556 | 12.2222 | -11 | 4.6227 | -8.0915 | -7.63 | -14.2252 | -20.0161

## Slide 10
Chart: Capacitor measurement error
| 60.00 | 75.00 | 100.00 | 200.00 | 300.00 | 400.00 | 500.00 | 600.00 | 700.00 | 800.00 | 900.00 | 1000.00 | 2000.00 | 3000.00 | 4000.00 | 5000.00 | 6000.00 | 7000.00 | 8000.00
Relative error compared to multimeter (%) | 0.63737 | 0.9965 | 2.7885 | 0.49505 | 1.5651 | 1.5 | 1.2048 | 1.3289 | 0.28531 | 1.0867 | -0.078678 | 8.1716 | 3.198 | 3.3898 | 1.6414 | 1.2146 | 1.3648 | 0.52068 | 1.3088
Relative error compared to printed value (%) | 0 | 0 | 1 | 1.5 | 1.6667 | 1.5 | 0.8 | 1.6667 | 0.42857 | 0 | -1.2222 | 5.9 | 1.65 | 1.666 | 0.625 | 0 | 0.26667 | -0.71429 | 0.625
Capacitor testing

## Slide 11: Output characteristic
Y axis is the collector current in mA. The X axis is the Collector-emitter voltage in V

## Slide 12: Input characteristic
In this case the collector and emitter is connected to ground. On the base increases the voltage and measures the current flowing through it.

## Slide 13: Transfer characteristics
In this case the collector-emitter voltage is constant and increases the base current. If this current is high enough then the transistor turns into a switch.

## Slide 14: Realizations
The tester can identify resistors, capacitors, diodes and transistors with approximate accuracy, while also identifies the pinout.
Displays the results on it’s built in display and only requires a USB power supply.
Simple usage and automated testing